## Slide 1
LECTURE 2
60-MINUTE MAIN LECTURE · LEAD INSTRUCTOR
Inside the
Simulator
Big question How can we model a real CPU using C++?
诺瓦留学 NOVARA · RISC-V CPU Verification

## Slide 2
LECTURE 2 · RISC-V AND SIMULATION
What this hour covers
01
What a simulator models
12 min
02
The verification flow
15 min
03
Our RV32I instruction set
15 min
04
Reading the trace
18 min
诺瓦留学 NOVARA · RISC-V CPU Verification
Lecture 2 · Roadmap
Notes: 用 1–2 分钟过一遍今天的节奏：告诉学生这节 60 分钟大课分成哪几块、各块大概多长时间，让他们心里有数。强调这是“主导师讲概念、助教带动手”的安排——今天先建立思路和方法，所有上机细节稍后交给助教在 lab 里逐步带。不要在这页停太久，快速进入正题。

## Slide 3
LECTURE 2 · THE IDEA
Software that behaves like hardware
A simulator is a program that imitates a CPU. We can run real instructions on it and check the results — long before any chip exists.
Simulator
Cheap and instant
Fully observable — see every register
Easy to change and re-run
Real silicon
Expensive to manufacture
Hard to see inside
Slow and costly to fix
诺瓦留学 NOVARA · RISC-V CPU Verification
Lecture 2
Notes: 约12分钟。定义仿真器：一个模仿 CPU 行为的程序。核心卖点用左右对比讲——仿真器便宜、即时、内部完全可见、随便改随便重跑；真实硅片昂贵、内部难观测、改一次代价巨大。让学生体会到：正因为可观测，仿真才是验证的主战场。强调“可见性”这个词，下面讲 trace 会再用到。

## Slide 4
LECTURE 2 · THE LOOP
What our testbench does, every time
This automatic cycle is the foundation of everything you will do for the rest of the course.
1
Load
Read an assembly program into the CPU.
2
Execute
Run it through the fetch-execute loop.
3
Check
Compare final register values to what we expect.
4
Report
Print PASS or FAIL for every test.
诺瓦留学 NOVARA · RISC-V CPU Verification
Lecture 2
Notes: 约15分钟。把验证台的工作讲成一个自动循环：装载程序→执行→检查最终寄存器值是否符合预期→逐条报告 PASS/FAIL。强调“预期值”这个概念——你必须事先知道正确答案，这是第三周测试设计的铺垫。让学生明白：测试不是把程序跑一遍看看，而是拿结果和事先算好的答案比对。第四步报告 PASS/FAIL 是工程化的关键，用绿色高亮一下。

## Slide 5
LECTURE 2 · THE TOOLKIT
Our RV32I instruction set
Arithmetic & logic
ADD SUB AND OR XOR SLL SRL SLT
Immediate
ADDI ANDI ORI SLLI SLTI
Memory
LW SW
Branch & jump
BEQ BNE BLT BGE JAL
20 instructions in total. Seven are the required core; the rest let you write richer tests and push your coverage higher.
诺瓦留学 NOVARA · RISC-V CPU Verification
Lecture 2
Notes: 约15分钟。不要逐条念指令，按家族讲：算术逻辑、立即数、访存、分支跳转。点明一共 20 条，其中 7 条（ADD SUB ADDI LW SW BEQ BNE）是必修核心，人人要懂；其余是给想做得更好的同学准备的，可以写出更丰富的测试、把覆盖率拉高——这一点直接关系到结课的推荐信标准。立即数和寄存器版的区别（ADD vs ADDI）点一下即可，细节交给助教在 lab 里讲。

## Slide 6
LECTURE 2 · THE KEY SKILL
Reading the execution trace
The trace shows what the CPU did at every step — the single most important skill in this course.
PC=0 ADDI x1, x0, 5 | x1 = 0 + 5 = 5
PC=1 ADDI x2, x0, 3 | x2 = 0 + 3 = 3
PC=2 ADD x3, x1, x2 | x3 = 5 + 3 = 8
PC=2
which instruction
ADD x3,x1,x2
what it ran
5 + 3 = 8
operands and result
诺瓦留学 NOVARA · RISC-V CPU Verification
Lecture 2
Notes: 约18分钟，本节核心，也是整门课最关键的技能。带着学生逐行读 trace：PC 告诉你是第几条指令，中间是执行了什么，竖线后面是操作数和结果。重点讲那行高亮的 x3 = 5 + 3 = 8——这就是 CPU 算出来的过程被写在纸面上。强调：当测试失败时，trace 会告诉你 CPU 到底做了什么，所以第四周调试完全靠它。让学生现在就习惯“看 trace 找证据”的思维。

## Slide 7
WITH YOUR TAs
In the lab: run your first simulation
Your TAs will get everyone building and running the testbench — your first real verification.
$ cd starter
$ make
$ ./riscv_testbench
[PASS] arithmetic_basic.asm
[PASS] memory_basic.asm
Summary: 6/6 tests passed.
In this session you will
1
Build the simulator from source with one command.
2
Run the test suite and read your first verification log.
3
Match each PASS line to the program that produced it.
4
Open a trace and find the final register values.
诺瓦留学 NOVARA · RISC-V CPU Verification
Lecture 2 · Lab handoff
Notes: 交接页：这是大课和 lab 的分界。你只需用一两分钟点题——说明接下来这部分由助教带大家在机器上动手完成，主导师不必讲实现细节。把屏幕上的命令和任务简单过一遍，让学生知道等会儿要做什么、目标是什么，然后把时间交给助教。提醒学生：遇到问题先看 trace、先讲证据，再问助教。

## Slide 8
You can run it.
Now make it prove itself.
Running tests that already pass is easy. Next week you become the one who writes them.
NEXT WEEK The art of testing — how do engineers know a processor is correct?
诺瓦留学 NOVARA · RISC-V CPU Verification
Notes: 收尾约 2 分钟：用屏幕上这句话给本周做一个有力、正向的总结，让学生感到自己确实学到了真本事。然后预告下周主题，制造期待——一句话点出下周要解决的新问题即可。