## Slide 1
LECTURE 3
60-MINUTE MAIN LECTURE · LEAD INSTRUCTOR
The Art
of Testing
Big question How do engineers know a processor works correctly?
诺瓦留学 NOVARA · RISC-V CPU Verification

## Slide 2
LECTURE 3 · VERIFICATION ENGINEERING
What this hour covers
01
Why testing is hard
12 min
02
What makes a good test
15 min
03
Expected vs actual
18 min
04
Test types & coverage
15 min
诺瓦留学 NOVARA · RISC-V CPU Verification
Lecture 3 · Roadmap
Notes: 用 1–2 分钟过一遍今天的节奏：告诉学生这节 60 分钟大课分成哪几块、各块大概多长时间，让他们心里有数。强调这是“主导师讲概念、助教带动手”的安排——今天先建立思路和方法，所有上机细节稍后交给助教在 lab 里逐步带。不要在这页停太久，快速进入正题。

## Slide 3
LECTURE 3 · THE CHALLENGE
You cannot just try it and see
A modern processor has billions of transistors and more possible states than you could ever check by hand. Verification engineers don't test everything — they design clever tests that catch bugs before manufacturing.
Billions
of transistors on a modern chip.
So the question becomes:
Which tests give us the most confidence?
诺瓦留学 NOVARA · RISC-V CPU Verification
Lecture 3
Notes: 约12分钟。先打破一个直觉：能不能把所有情况都跑一遍看看？不能——现代芯片有数十亿晶体管，状态空间天文数字。验证工程师的工作不是穷举，而是设计聪明的测试，用最少的测试拿到最大的信心。把问题收束成右下角那句话：哪些测试最能给我们信心？这为下面“好测试的标准”做铺垫。

## Slide 4
LECTURE 3 · THE RECIPE
What every good test needs
A clear purpose
It checks one specific behaviour — say, that ADD adds.
A known expected result
You predict the answer before you run it. This is the oracle.
A pass / fail outcome
The test decides for itself whether the CPU was right.
诺瓦留学 NOVARA · RISC-V CPU Verification
Lecture 3
Notes: 约15分钟。好测试的三要素：明确目的（一次只验一个行为，比如验证 ADD 真的在加）；已知的预期结果（运行前就把答案算出来——这就是 oracle / 判定基准，是验证的灵魂）；自动的通过/失败结论（测试自己判断对错，不靠人眼）。中间那条 oracle 用深色圈重点强调。可以追问学生：如果你不知道正确答案，你怎么知道 CPU 错了？引出下一页的“预期 vs 实际”。

## Slide 5
LECTURE 3 · THE HEART OF IT
Expected vs actual
Write a program, predict the result, run it, and compare. A testbench is really just this comparison, automated.
YOU EXPECT
x3 = 8
ADD of 5 and 3
THE CPU PRODUCES
x3 = 8
they match → PASS
If they ever differ, something is wrong — the program, or the CPU. Your job is to find out which.
诺瓦留学 NOVARA · RISC-V CPU Verification
Lecture 3
Notes: 约18分钟，本节核心。流程四步：写程序→预测结果→运行→比对。验证台本质上就是把这个比对自动化。用屏幕的例子：你预期 x3=8，CPU 也给出 8，匹配就 PASS。然后抛出关键情形：一旦两者不一致，要么是你的程序写错了，要么是 CPU 有 bug——你的任务是判断是哪一个。这一句直接通向第四周的调试。让学生体会：验证的价值就在“不一致”被发现的那一刻。

## Slide 6
LECTURE 3 · BUILDING A SUITE
Cover the behaviours that matter
Arithmetic
ADD, SUB, immediates
Memory
LW and SW round-trips
Branch
taken and not-taken
Edge cases
zero, negatives, limits
Coverage asks a simple question: which instructions has your suite actually exercised? It reveals the gaps you forgot.
诺瓦留学 NOVARA · RISC-V CPU Verification
Lecture 3
Notes: 约15分钟。先给测试分类：算术、内存（写进去再读出来）、分支（跳与不跳两种都要测）、边界（0、负数、极值）。强调边界用例最容易暴露 bug。然后引入覆盖率的直观定义：你的测试到底碰过哪些指令？它能把你“忘了测的”指针出来。点到为止——具体怎么生成 coverage 报告、怎么读，交给第五周和助教 lab。让学生现在记住“覆盖率=找盲区”。

## Slide 7
WITH YOUR TAs
In the lab: write your own tests
Your TAs will help you turn ideas into real test programs and grow your suite.
starter/programs/
student_custom_test.asm
ADDI x1, x0, 10
ADDI x2, x0, 20
ADD x3, x1, x2 # expect 30
In this session you will
1
Choose a behaviour you want to verify.
2
Write the assembly program for it.
3
Predict the expected result before running.
4
Run, compare, and add it to your suite.
诺瓦留学 NOVARA · RISC-V CPU Verification
Lecture 3 · Lab handoff
Notes: 交接页：这是大课和 lab 的分界。你只需用一两分钟点题——说明接下来这部分由助教带大家在机器上动手完成，主导师不必讲实现细节。把屏幕上的命令和任务简单过一遍，让学生知道等会儿要做什么、目标是什么，然后把时间交给助教。提醒学生：遇到问题先看 trace、先讲证据，再问助教。

## Slide 8
You can prove
it works.
But every engineer eventually meets a test that fails. Next week, we make sure of it.
NEXT WEEK Finding the bug — we have hidden one in the CPU. Your job is to catch it.
诺瓦留学 NOVARA · RISC-V CPU Verification
Notes: 收尾约 2 分钟：用屏幕上这句话给本周做一个有力、正向的总结，让学生感到自己确实学到了真本事。然后预告下周主题，制造期待——一句话点出下周要解决的新问题即可。