## Slide 1
LECTURE 4
60-MINUTE MAIN LECTURE · LEAD INSTRUCTOR
Finding
the Bug
Big question What should an engineer do when a test fails?
诺瓦留学 NOVARA · RISC-V CPU Verification

## Slide 2
LECTURE 4 · DEBUGGING METHODOLOGY
What this hour covers
01
Evidence, not guesses
10 min
02
The five-step loop
15 min
03
The trace as evidence
20 min
04
Root cause vs symptom
15 min
诺瓦留学 NOVARA · RISC-V CPU Verification
Lecture 4 · Roadmap
Notes: 用 1–2 分钟过一遍今天的节奏：告诉学生这节 60 分钟大课分成哪几块、各块大概多长时间，让他们心里有数。强调这是“主导师讲概念、助教带动手”的安排——今天先建立思路和方法，所有上机细节稍后交给助教在 lab 里逐步带。不要在这页停太久，快速进入正题。

## Slide 3
THE GOLDEN RULE OF DEBUGGING
Do not guess. Use evidence.
Debugging is not luck and it is not magic. It is the scientific method: observe what happened, form a hypothesis, test it, and narrow down until the cause is undeniable.
诺瓦留学 NOVARA · RISC-V CPU Verification
Notes: 约10分钟，定调子。整堂课就一句话：不要猜，用证据。调试不是靠运气也不是玄学，而是科学方法——观察现象、提出假设、验证、不断缩小范围直到原因确凿。用深色全屏强调这句话，让学生形成肌肉记忆。可以讲个小故事：新手一遇到 bug 就乱改代码碰运气，老手先看证据。这页是本周的精神内核，后面所有步骤都是它的展开。

## Slide 4
LECTURE 4 · THE METHOD
The five-step debugging loop
1
Reproduce
Make the failure happen reliably.
2
Observe
Look at exactly what the CPU did.
3
Compare
Expected vs actual — where do they diverge?
4
Locate
Trace the divergence back to its root cause.
5
Fix & retest
Correct it, then prove the fix worked.
诺瓦留学 NOVARA · RISC-V CPU Verification
Lecture 4
Notes: 约15分钟。给学生一个可复用的五步流程：复现（让失败稳定出现）、观察（看 CPU 到底做了什么）、比对（预期 vs 实际在哪一步分叉）、定位（顺着分叉点找到根因）、修复并回归（改完再跑一遍证明修好了）。强调顺序不能跳，尤其不能跳过观察直接改代码。最后一步“修复并回归”用绿色，呼应验证思维——改完必须再验证。告诉学生这套流程任何工程领域都通用。

## Slide 5
LECTURE 4 · THE EVIDENCE
Let the trace catch the bug
A test fails. Instead of guessing, we read the trace — and the contradiction is right there.
[FAIL] arithmetic_basic.asm — expected x3=8 but got 2
PC=0 ADDI x1, x0, 5 | x1 = 0 + 5 = 5
PC=1 ADDI x2, x0, 3 | x2 = 0 + 3 = 3
PC=2 ADD x3, x1, x2 | x3 = 5 + 3 = 2 <-- impossible
The line says "+" but 5 + 3 is not 2. The ADD instruction must be doing the wrong operation.
诺瓦留学 NOVARA · RISC-V CPU Verification
Lecture 4
Notes: 约20分钟，本节核心，配合 lab 的植入 bug。场景：arithmetic 测试失败，预期 x3=8 实际 2。不要猜，直接读 trace——那行写着 5 + 3 = 2，明显不可能：符号是加号，结果却像减法。证据把矛头直接指向 ADD 指令做错了运算。带学生体会“看 trace→发现自相矛盾→锁定指令”的完整推理链。提示：这个 bug 在 loop_sum 里也会显形，引出下一页根因 vs 症状。让学生现在就跃跃欲试去 lab 抓它。

## Slide 6
LECTURE 4 · THINK DEEPER
Root cause, not symptom
The symptom
"The test gives the wrong number." True — but patching the test hides the problem instead of solving it.
The root cause
"ADD computes a − b instead of a + b." Fix that one line and every failing test passes at once.
One root cause can produce many symptoms — here, both the arithmetic test and the loop test fail for the same reason.
诺瓦留学 NOVARA · RISC-V CPU Verification
Lecture 4
Notes: 约15分钟。区分症状和根因：症状是“测试给了错的数”，但去改测试只是掩盖问题；根因是“ADD 实际算的是 a−b”，改对那一行，所有相关失败一次性消失。强调工程师要修根因不修症状。再点一次“一个根因，多个症状”——arithmetic 和 loop_sum 都失败，是同一个原因。这培养系统性思维。结尾把学生交给 lab：去亲手抓这个 bug、写调试报告。

## Slide 7
WITH YOUR TAs
In the lab: the debugging challenge
A bug has been planted in the CPU. Your TAs are there to coach your reasoning — not to hand you the answer.
$ ./riscv_testbench
[FAIL] arithmetic_basic.asm
expected x3=8 but got 2
PC=2 ADD x3,x1,x2 | 5 + 3 = 2
[PASS] memory_basic.asm
In this session you will
1
Run the testbench and find which test fails.
2
Read the trace and spot the contradiction.
3
Explain the root cause in your own words.
4
Fix the code, retest, and write your debugging report.
诺瓦留学 NOVARA · RISC-V CPU Verification
Lecture 4 · Lab handoff
Notes: 交接页：这是大课和 lab 的分界。你只需用一两分钟点题——说明接下来这部分由助教带大家在机器上动手完成，主导师不必讲实现细节。把屏幕上的命令和任务简单过一遍，让学生知道等会儿要做什么、目标是什么，然后把时间交给助教。提醒学生：遇到问题先看 trace、先讲证据，再问助教。

## Slide 8
You can find
and fix faults.
You have done the engineering. The last skill is making others understand it.
NEXT WEEK Coverage and communication — measure what you tested, and present like an engineer.
诺瓦留学 NOVARA · RISC-V CPU Verification
Notes: 收尾约 2 分钟：用屏幕上这句话给本周做一个有力、正向的总结，让学生感到自己确实学到了真本事。然后预告下周主题，制造期待——一句话点出下周要解决的新问题即可。